## Slide 1
MULTICORE ARCHITECTURE & PROGRAMMING
L-T-P 2-0-1

## Slide 2
Chapter No. 1: Introduction to Multicore
Drivers for Multicore Architectures: Low power, Performance/Throughput and need for memory bandwidth – Limits of single core computing – Moore’s law - Limits to Instruction Level Parallelism (ILP) – Power and heat dissipation issue – Increased amount of data to process – Evolution from traditional System-On-Chip (SoC) to MPSoCs (Multi processor System-On-Chips) - Need for Multicore controllers in Automotive domain

## Slide 3: Agenda
 Future of Automotive E/E architecture
 Drivers for Multicore
 Multicore Architecture Overview
 Multicore Hardware used in Automotive
 Scheduling

## Slide 4: Drivers for Multicore
 Future of Automotive E/E architecture
 Moore’s law
 Challenges:
Power Consumption and Heat dissipation
Memory wall
Limits to Instruction level Parallelism
 The act of balancing
 Single core Vs Multicore – A quick comparison
 Summary

## Slide 5: Automotive E/E Architecture

## Slide 6: Future mobility
Electrified, Automated and Connected
https://www.gsaglobal.org/wp-content/uploads/2019/05/Trends-of-Future-EE-Architectures.pdf

## Slide 7: Automotive E/E architecture – Future trends Challenges and Bottlenecks
https://www.gsaglobal.org/wp-content/uploads/2019/05/Trends-of-Future-EE-Architectures.pdf

## Slide 8
https://www.gsaglobal.org/wp-content/uploads/2019/05/Trends-of-Future-EE-Architectures.pdf

## Slide 9: Drivers for Multicore

## Slide 10: Multicore - Drivers Moore’s law
 Moore's law is the observation that the number of transistors in a dense integrated circuit (IC) doubles about every two years
 As the number of transistors increases, the number of cores increases accordingly
https://en.wikipedia.org/wiki/Moore%27s_law
https://ocw.mit.edu/courses/electrical-engineering-and-computer-science/6-172-performance-engineering-of-software-systems-fall- 2018/lecture-slides/MIT6_172F18_lec6.pdf

## Slide 11: Multicore - Drivers Increased Power and Heat consumption
1 The Free Lunch Is Over - A Fundamental Turn Toward Concurrency in Software, Herb Sutter, 2009, http://www.gotw.ca/publications/concurrency-ddj.htm *https://www.nxp.com/files-static/32bit/doc/ref_manual/EMBMCRM.pdf
Free Lunch is Over!
The Limits
 Power wall
 Instruction Level Parallelism wall
 Memory bandwidth wall
1
Sequential computing is hitting the limits
http://www.ecs.umass.edu/ece/andras/courses/ECE668/Mylectures/Introduction_to_Multi_Core.pdf

## Slide 12: Moore's Law
Moore’s Law
Slide source: UCB CS 194 Fall’2010
In 1965, Intel co-founder Gordon Moore predicted (from just 3 data points!) that semiconductor density would double every 18 months.
  He was right! Transistors are still shrinking as he projected.

## Slide 13: Consequences of Moore’s law…

## Slide 14: The Hardware/Software contract
Write your software as you choose and we HW-geniuses will take care of performance.
9
The result: Generations of performance ignorant software engineers using performance-handicapped languages (such as
Java) … which was OK since performance was a HW job.
Third party names are the property of their owners.

## Slide 15: … Computer architecture and the power wall
0
15
20
25
30
0
2
6
8
4
Scalar Performance
Power
power = perf ^ 1.74
Pentium M
i486
Pentium
10
Pentium Pro
5
Pentium 4 (Wmt)
Pentium 4 (Psc)
Growth in power is unsustainable
Source: E. Grochowski of Intel
15

## Slide 16: … partial solution: simple low power cores
0
5
10
15
20
25
30
0
2
6
8
4
Scalar Performance
Power
power = perf ^ 1.74
Pentium M
i486
Pentium
Pentium Pro
Pentium 4 (Wmt)
Pentium 4 (Psc)
Mobile CPUs
with shallow
pipelines use less
power
Eventually Pentium 4 used
Source: E. Grochowski of Intel
16
over 30 pipeline stages!!!!

## Slide 17: For the rest of the solution consider power in a chip …
Processor
f
Input
Output
Capacitance = C Voltage = V Frequency = f Power = CV2f
C = capacitance … it measures the
ability of a circuit to store energy:
C = q/V € q = CV
Work is pushing something (charge or q) across a “distance” … in electrostatic terms pushing q from 0 to V:
V * q = W.
But for a circuit q = CV so
W = CV2
power is work over time … or how many
times in a second we oscillate the circuit
Power = W* F € Power = CV2f

## Slide 18: ... The rest of the solution
add cores
Processor
f
Processor
f/2
Processor
f/2
f
Input
Output
Input
Output
Capacitance = C Voltage = V Frequency = f Power = CV2f
Capacitance = 2.2C Voltage = 0.6V Frequency = 0.5f Power = 0.396CV2f
Chandrakasan, A.P.; Potkonjak, M.; Mehra, R.; Rabaey, J.; Brodersen, R.W., "Optimizing power using transformations," IEEE Transactions on Computer-Aided Design of Integrated Circuits and Systems,, vol.14, no.1, pp.12-31, Jan 1995
Source: Vishwani Agrawal

## Slide 19: Microprocessor trends
IBM Cell
NVIDIA Tesla C1060
Intel SCC Processor
AMD ATI RV770
3rd party names are the property of their owners.
Individual processors are many core (and often heterogeneous) processors.
80 cores
30 cores
8 wide SIMD
1 CPU + 6 cores
10 cores
16 wide SIMD
48 cores
Source: OpenCL tutorial, Gaster, Howes, Mattson, and Lokhmotov
ARM MPCORE
Intel® Xeon® processor
4 cores
4 cores

## Slide 20: The result…
15
+
=
A new contract … HW people will do what’s natural for them (lots of simple cores) and SW people will have to adapt (rewrite everything)
The problem is this was presented as an ultimatum … nobody asked us if we were OK with this new contract … which is kind of rude.

## Slide 21: Multicore - Drivers Over-clocking in Single cores vs Multicores
Improved Power Consumption as an Incentive for Multicore (MPC8641) *
*https://www.nxp.com/files-static/32bit/doc/ref_manual/EMBMCRM.pdf
 Doubling the frequency causes a fourfold increase in power consumption
 Higher frequencies need increased voltage because processors with higher speed transistors leak more than slow ones

## Slide 22: Multicore Limits to Instruction level Parallelism
https://slideplayer.com/slide/777647/
*https://www.nxp.com/files-static/32bit/doc/ref_manual/EMBMCRM.pdf
Instruction level Parallelism refers to the number of instructions that can be executed in parallel
How to achieve it:
Compiler level optimization
Hardware techniques
Limitations are:
Data dependency
Procedural dependency
Resource conflicts
General organization of a 3 way superscalar processor
Pic Source: https://www.oreilly.com/library/view/algorithms-and-parallel/9780470934630/c02-sec1-0007.xhtml

## Slide 23: Instruction level Paral

## Slide 24: Multicore - Drivers Increased data to process – More memory access
Memory Wall:
 Increase in the on-core speed is not matched by the speed of off-core and off-chip memory and
IO subsystems
 High-frequency core matched with a lower-frequency bus will frequently stall as the core waits for data
 Fast On-chip caches can reduce this issue at the cost of increased power consumption

## Slide 25: Multicore - Drivers The act of balancing
Increased Performance
Reduced Power and Heat consumption
Goal is to achieve higher performance with lower power consumption

## Slide 28: Why multi-core ?
Difficult to make single-core clock frequencies even higher
Deeply pipelined circuits:
    Heat problems
    Clock problems
    Efficiency (Stall) problems
Doubling issue rates above today’s 3-6 instructions per clock, say to 6 to 12 instructions, is extremely difficult
    Issue 3 or 4 data memory accesses per cycle,
    Rename and access more than 20 registers per cycle, and
    Fetch 12 to 24 instructions per cycle.
Many new applications are multithreaded
General trend in computer architecture (shift towards more parallelism)

## Slide 29: Multi-Core Processor is a Special Kind of Multiprocessor
What is multi-core Processor?
A multicore processor is a single integrated circuit (a.k.a., chip multiprocessor or CMP) that contains multiple core processing units, more commonly known as cores.

## Slide 30
Replicate multiple processor cores on a single die.
Multi-Core Architectures

## Slide 31: Multicore SingleCore Vs Multicore – A quick comparison
Parameter | Single core processor | Multicore processor
Number of cores on a die | Single | Multiple
Instruction Execution | Can execute single thread or task at a time | Can execute multiple tasks by using multiple cores
Gain | Speed up every program or software being executed | Speed up the programs which are designed for multi-core processors
Performance | Dependent on the clock frequency of the core | Dependent on the frequency, number of cores and program to be executed
http://www.ecs.umass.edu/ece/andras/courses/ECE668/Mylectures/Introduction_to_Multi_Core.pdf

## Slide 32: Multicore - Drivers Summary
 Power is costly; Transistors, relatively cheap
 Frequency alone is not important; Efficiency IS
 Performance-per-watt is critical; per-core performance is not quite
 Computation is relatively easy; Memory accesses are NOT
Sequential computing is hitting the limits. Multi-/Manycore is the present & Future
http://fmcet.in/CSE/CS6801_uw.pdf

## Slide 33: Multicore Architectures

## Slide 34: Agenda Multicore Architecture
 Types of Multicore
 Communication architecture
 Memory Architecture
 Why Multicore Software & Hardware architectures go hand-in-hand?
 Summary

## Slide 35: Multicore Architectures Types of Multicore
Cores are not identical and
implement different instruction sets
Cores are identical and execute the same instruction set
*https://www.nxp.com/files-static/32bit/doc/ref_manual/EMBMCRM.pdf

## Slide 36: Multicore Architectures Heterogeneous Multicore Example
Cores that have been optimized for different things are combined to create the best of different worlds
Benefits
 Performance optimization
 Improved system reliability and security
 Low power consumption
NXP’s i.MX7 is a heterogeneous Multicore SoC. It has:
 an ARM Cortex-A7 (one or two cores)
Run an OS like Linux on the Cortex-A7 core
 One ARM Cortex-M4 core
Real-time OS like FreeRTOS on the Cortex-M4
efficient
https://www.witekio.com/blog/introduction-heterogeneous-multicore-processing-architecture/ https://www.embeddedartists.com/heterogeneous-multi-core-processing/ https://blog.nxp.com/tech-insights/3-reasons-why-embedded-heterogeneous-systems-are-more-

## Slide 37: Multicore Architectures Homogeneous Multicore Example
Infineon AURIX Multicore controllers – TC2XX, TC3XX series
 3 cores to 6 cores controllers
 Access to the complete memory and peripherals
 SPI (Serial Peripheral Interface) crossbar to connect the cores
The suffix P stands for Performance and the E for Efficiency. The difference between the two cores is that the Efficiency cores are power consumption optimized. Tricore 1.6E has less pipeline stages (4 stages at E- and 6 stages at P-core) and is operating at a lower frequency (200 MHz for E- instead of 300 MHz for P-core). In addition the Tricore 1.6E is a single issue architecture.

## Slide 38: Classifying Parallel Systems – Flynn’s Taxonomy
Distinguishes multi-processor computer architectures along the two independent dimensions
  Instruction and Data
  Each dimension can have one state: Single or Multiple
SISD: Single Instruction, Single Data
  Serial (non-parallel) machine
SIMD: Single Instruction, Multiple Data
  Processor arrays and vector machines
MISD: Multiple Instruction, Single Data (weird)
MIMD: Multiple Instruction, Multiple Data
  Most common parallel computer systems

## Slide 39: Parallel Architecture Types
Instruction-Level Parallelism
  Parallelism captured in instruction processing
Vector processors
  Operations on multiple data stored in vector registers
Shared-memory Multiprocessor (SMP)
  Multiple processors sharing memory
  Symmetric Multiprocessor (SMP)
Multicomputer
  Multiple computer connect via network
  Distributed-memory cluster
Massively Parallel Processor (MPP)

## Slide 40: How do you get parallelism in the hardware?
Instruction-Level Parallelism (ILP)
Data parallelism
  Increase amount of data to be operated on at same time
Processor parallelism
  Increase number of processors
Memory system parallelism
  Increase number of memory units
  Increase bandwidth to memory
Communication parallelism
  Increase amount of interconnection between elements
  Increase communication bandwidth

## Slide 41: Parallel Architecture Types
Shared Memory Multiprocessor (SMP)
  Shared memory address space
  Bus-based memory system
  Interconnection network
Uniprocessor
  Scalar processor
  Vector processor
  Single Instruction Multiple Data (SIMD)
processor
memory
processor
memory
vector
processor
processor
memory
bus
processor
processor
memory
network
…
…
…
processor
memory
…

## Slide 42: Parallel Architecture Types (2)
Distributed Memory Multiprocessor
  Message passing between nodes
  Massively Parallel Processor (MPP)
    Many, many processors
Cluster of SMPs
  Shared memory addressing within SMP node
  Message passing between SMP nodes
  Can also be regarded as MPP if processor number is large
processor
memory
processor
memory
processor
memory
processor
memory
interconnection network
…
…
…
…
…
…
interconnection network
M
M
M
M
P
P
P
P
P
P
P
P
…
…
network
interface

## Slide 43: Parallel Architecture Types (3)
Multicore SMP+GPU Cluster
  Shared memory addressing within SMP node
  Message passing between SMP nodes
  GPU accelerators attached
Multicore
  Multicore processor
  GPU accelerator
  “Fused” processor accelerator
memory
C
C
C
C
m
m
m
m
processor
memory
PCI
…
…
…
…
…
…
interconnection network
M
M
M
M
P
P
P
P
P
P
P
P
processor
memory
cores can be hardware multithreaded (hyperthread)

## Slide 44: How do you get parallelism in the hardware?
Instruction-Level Parallelism (ILP)
Data parallelism
  Increase amount of data to be operated on at same time
Processor parallelism
  Increase number of processors
Memory system parallelism
  Increase number of memory units
  Increase bandwidth to memory
Communication parallelism
  Increase amount of interconnection between elements
  Increase communication bandwidth

## Slide 45: Multicore communication architecture
Shared Memory System
Distributed Memory System

## Slide 46: Multicore communication architecture
Communication between Processing elements in Multicore
 Affects scalability of the system
o How many more additional cores/processing elements can be added?
 Affects performance and energy efficiency
How fast can processors, caches, and memory communicate?
Data latency: How long are the latencies to memory?
How much energy is spent on communication?
Communication Arch. Impacts scalability and performance!
Connection between processing elements, connection between Processing elements and
Memory/Peripherals
Types of communication:
Point-To-Point
Bus
Cross bar
NoC (Network-On-Chip)
https://www.cs.umd.edu/class/spring2015/cmsc411-0201/lectures/lecture22-interconnects.pdf

## Slide 47: Multicore communication architecture Point-To-Point communication
 Point-to-Point Connections
Every node connected to every other node
Lowest Latency
High cost
Not scalable
HyperTransport – Used in Nvidia nForce chipsets, AMD’s Athlon chips
https://www.cs.umd.edu/class/spring2015/cmsc411-0201/lectures/lecture22-interconnects.pdf

## Slide 48: Multicore communication architecture Communication between Processing elements in Multicore
 Shared bus
Simple
Cost effective for a small number of nodes
Not scalable
High contention resulting in fast saturation
https://www.cs.umd.edu/class/spring2015/cmsc411-0201/lectures/lecture22-interconnects.pdf
Pic source: Real world Multicore embedded systems – Bryon Moyer

## Slide 49: Multicore communication architecture
Communication between Processing elements in Multicore
 Crossbar
Every node connected to every other
Enables concurrent sends to non-conflicting destinations
Good for small number of nodes
Low latency and high throughput
Not scalable
https://www.cs.umd.edu/class/spring2015/cmsc411-0201/lectures/lecture22-interconnects.pdf

## Slide 50: Multicore communication architecture Communication between Processing elements in Multicore
 Network-On-Chip (NoC)
A NoC is constructed from multiple point-to- point data links interconnected by switches (routers), such that messages can be relayed from any source module to any destination module over several links, by making routing decisions at the switches
Reduces wiring complexity
Predictable speed
Reliability
https://sites.google.com/site/alexandrutopirceanu/research/networks-on-chips
`www.ecs.umass.edu/ece/andras/courses/ECE668/Mylectures/Introduction_to_Multi_Core.pdf

## Slide 51: Multicore Memory Architecture Why memory architecture is important for Multicore?
 Memory speeds did not advance as fast as the processing elements
o Consequence: Data access latency: Processor outruns memory, leading to decreased utilization
Symmetric Multi-Processing (SMP)
Identical memory access latencies for
all processors
Performance penalty if performance depends on memory bandwidth
Non-Uniform Memory Access (NUMA)
Faster access to local memory
Higher latencies to remote memories
Memory is much slower compared to processing element
Pic source: Real world Multicore embedded systems – Bryon Moyer

## Slide 52: Multicore Memory Architecture Cache
http://course.ece.cmu.edu/~ece600/lectures/lecture17.pdf
 Caches are helpful with multicores
Reduce access latency, reduce load on bus
For both private and shared data across cores
 Advantages of private caches:
Core local enabling faster access
Reduces contention to cache by cores
 Advantages of shared cache:
Tasks on different cores can share the same cache data
More cache space available if a single (or a few) high-performance thread runs on the system
 Multiple private caches introduce the problems of Cache Coherence

## Slide 53: Multicore Memory Architecture Cache
http://course.ece.cmu.edu/~ece600/lectures/lecture17.pdf

## Slide 54: Multicore Memory Architecture Cache
http://course.ece.cmu.edu/~ece600/lectures/lecture17.pdf
Snooping cache coherence
The idea behind snooping comes from bus-based systems:
When the cores share a bus, any signal transmitted on the bus can be “seen” by all the cores connected to the bus.
Thus, when core 0 updates the copy of x stored in its cache, if it also broadcasts this information across the bus, and if core 1 is “snooping” the bus, it will see that x has been updated and it can mark its copy of x as invalid. This is more or less how snooping cache coherence works.
Directory-based cache coherence protocols attempt to solve this problem through the use of a data structure called a directory. The directory stores the status of each cache line.

## Slide 55: Multicore Architecture
Need for Multicore Software Architectures
 Multicore Software-Hardware architecture required for:
 Managing Cost, Performance and Power requirements
 Processor speed isn’t increasing
 Power, Heat dissipation issues
 Less advantages from ILP (Instruction Level Parallelism)
 Increased amount of data and its processing requirement (Memory bandwidth and Memory architecture )
 More Thread Level Parallelism needed
 Multicore Software Architecture
 With Multicore, challenges are shifted from Hardware to Software : Concurrency, Latency. Debugging, Simulation, Optimization…
 Software development keeping parallelism in mind to make the best use of underlying hardware
Multicore Hardware and Software architectures go hand in hand

## Slide 56: Scheduling

## Slide 57: Multicore Key definitions used in slides
 Processing elements/CPU/Core/Processor all mean the same and are interchangeably used
 Task is the smallest schedulable execution unit. Operating system scheduler manages task execution.
 Latency In an embedded system, the time between receiving input values and sending output values is called task execution latency. The execution latency strongly depends on the performance of the used hardware and on interruptions by tasks with higher priority or by interrupts
 Jitter is an undesired variation in the sampling time t (sampling jitter), and/or the end-to-end latency L (response time jitter). Jitter in the end-to-end latency L can decrease the quality of control and can cause instability of the control loop
 Raster loss: Communication between two tasks can have an additional latency time by a period if these tasks have the same time period and run asynchronously parallel on two different cores

## Slide 58: Multicore basics - Scheduling Let’s start with real time embedded systems….
2
 Embedded systems are classified based on the acceptability of missing its timing constraints into:
Soft real time - Missing a timing constraint is acceptable but undesirable
Firm real time – Missing a timing constraint results in loss of value or usefulness of the solution
Hard real time - Missing timing constraint is unacceptable, safety critical
https://www.allaboutcircuits.com/technical-articles/introduction-to-real-time-embedded-systems/

## Slide 59: Multicore basics - Scheduling Introduction
2
 Scheduler is also known as “Dispatcher”
 It’s the part of the kernel which determines which task to run next
 When more than one task becomes “runnable” then the scheduler determines which task to run (execute) first
 The algorithm that it uses for determining the next task to execute is known as the “Scheduling Algorithm”

## Slide 60: Multicore basics - Scheduling Types of Scheduling – Static Scheduling
 With static scheduling, the scheduling algorithm has complete knowledge of all tasks to be
scheduled and their constraints
 The priority of a task is set at compile time and does not change during application execution
 It is sufficient at runtime to start the tasks at the predetermined points in time, in their predetermined order
 Usual constraints are...
Deadline
Future release times
Computation time

## Slide 61: Multicore basics - Scheduling Dynamic scheduling
 A dynamic scheduling algorithm has only knowledge of the ready processes but it has no knowledge of future activation times
 Since new processes may become ready spontaneously, the scheduler has to decide at runtime which process has to be selected among the ready processes
 Each task can change its priority during execution
 Disadvantages are higher computational requirements and the memory demand for the management of processes

## Slide 62: Multicore basics - Scheduling Scheduling algorithms (1/2)
 First come First Serve (FCFS)
Tasks are executed in the order that they arrive
Context switches only occur upon task termination. Less scheduling overhead
Turnaround time, waiting time and response time can be high
No prioritization occurs, thus this system has trouble meeting task deadlines
 Round Robin Scheduling
The scheduler assigns a fixed time unit per task, and cycles through them
Involves extensive overhead, especially with a small time unit
High waiting times. Deadlines are rarely met
No priority given to tasks. Hence no starvation

## Slide 63: Multicore basics - Scheduling Scheduling algorithm (2/2)
 Earliest Deadline first
Tasks with the closest deadline will be executed first
Dynamic scheduling algorithm
 Fixed priority preemptive scheduling
Fixed priority assigned to every task and tasks are executed in order of their priority
Lower-priority tasks get interrupted by incoming higher-priority tasks
Waiting time and response time depend on the priority of the process. Higher-priority processes have smaller waiting and response times
Deadlines can be met by giving processes with strict deadlines a higher priority
Starvation of lower-priority processes is possible with large numbers of high-priority processes queuing for CPU time
 Rate monotonic scheduling
Priorities are assigned on the basis of the cycle duration of the task
Shorter the cycle duration, higher the task’s priority

## Slide 64: Multicore basics - Scheduling Non-preemptive scheduling
Adapted from Source: Real Time Systems and Real –Time Operating System - CranesSoftware

## Slide 65: Multicore basics - Scheduling Non-Preemptive scheduling
 Also known as Cooperative scheduling
 A task is responsible for relinquishing the CPU (at the process border)
 Easier to implement and has a smaller footprint
 Tasks have an assigned priority
 Advantage : Less need to “guard” shared resources
 Disadvantages : Tasks must relinquish the CPU at the process border, relatively lower
response time as compared to pre-emptive tasks

## Slide 66: Multicore basics - Scheduling Preemptive scheduling
Adapted from Source: Real Time Systems and Real –Time Operating System - CranesSoftware

## Slide 67: Multicore basics - Scheduling Preemptive scheduling
 Temporarily suspends the current task and enables the next “eligible” task to execute
 The criteria for suspension and eligibility determination is provided by the Scheduling Algorithm
 The highest priority task will be eligible to run.
 Advantages: Responsiveness is optimal & deterministic
 Disadvantages: Shared resources must be properly guarded

## Slide 68: Multicore basics - Scheduling Sharing task priorities
 Tasks of same priority run in mutual exclusion from each other
 Tasks that share priorities are released from the ready state in first-in, first-out (FIFO) order

## Slide 69: Multicore basics - Scheduling Pre-emptive & Non-preemptive scheduling
Parameter | Pre-emptive scheduling | Non Pre-emptive scheduling
Approach | Task is allocated the core for a limited period of time | Once a core is allocated to a task, the task holds it until it finishes or it goes to wait state (relinquishes control of the core voluntarily)
Interrupt | Interruption of low priority task by a high priority task is possible | Task cannot be interrupted until it finishes or voluntarily relinquishes control
Starvation | Starvation of low priority tasks can happen if high priority tasks are more and are triggered often | Starvation could happen if low priority tasks are not provided enough CPU resources
Overhead | Both run time and memory overhead - more context switches | Relatively less overhead
Advantages | Faster response time | Relatively slower response time
https://www.geeksforgeeks.org/preemptive-and-non-preemptive-scheduling/

## Slide 70
Multicore basics - Scheduling
Pre-emptive Vs Non Preemptive scheduling
Mixture of Non-Preemptive and Pre-emptive scheduling is used in many applications
Refer Link

## Slide 71: Multicore basics - Scheduling Different Types of Tasks
 Basic Tasks
Start, Execute and Terminate – Single shot tasking model
Relinquishes processor only when task is complete or pre- empted
Fast and Efficient
 Extended Tasks
Start, execute, wait for events and (optionally) terminate
Can voluntarily suspend itself. Useful when synchronization
points are needed
Basic/Extended tasks is a nomenclature used in Automotive
standards like OSEK/AUTOSAR
https://www.researchgate.net/figure/Basic-and-extended-task-model-adapted-from-OSE05_fig17_261989601

## Slide 72: Multicore basics - Scheduling Task Vs Interrupt priorities
NMI/Trap
Interrupt Z
Interrupt Y
Interrupt X
Task A
Task B
Task D
Task C
Increasing priority
 A system can contain:
Planned Tasks
Interrupts as a response to external events
NMI (Non-Maskable Interrupts)/Traps arising from errors
 High priority task can interrupt low prio tasks
 Tasks can be pre-empted by Interrupts
 High priority interrupts can pre-empt low priority interrupts
 NMI/Trap has the highest priority and is always serviced first by the hardware

## Slide 73: Multicore basics - Scheduling Activation of Tasks
 Tasks are activated:
Periodically – Time triggered using an Alarm or a counter
Event triggered - External events
 Tasks are scheduled by the OS after activation
 The scheduler determines the next task and starts/resumes it.

## Slide 74: Multicore basics - Scheduling Scheduling in Multicore
Task 1
Task 2
Task 3
CPU
Task 1
ISR2
Task 3
CPU 1 | 
CPU 2
ISR1
Task 2
Task 4
Single core
Multicore

## Slide 75: Multicore basics - Scheduling Types of Multicore scheduling
 Global Scheduling
Every Task can execute on every available core. It has relatively higher runtime overhead
 Partitioned Scheduling
Tasks are statically assigned to exactly one core. Execution core doesn‘t change dynamically
 Semi Partitioned Scheduling/Clustered scheduling
Limited Task migration within cores that belong to a cluster is feasible. It has some runtime overhead
Pic Source: https://slideplayer.com/slide/4805759/

## Slide 76: Multicore basics - Scheduling Key differences in scheduling in Single core and Multicore
ms
ms
5 ms
10 ms
ms
ms
5 ms
10 ms
Core0
Core1
Single Core
Priority
Priority

## Slide 77: Multicore basics - Scheduling Exercise – Single core scheduling  When will be Task A / Task C finished?
Task name | Core | Prio | Preemptive/ cooperative | Start time | Duration
A | 0 | 5 (High) | pre-emptive | 5 | 20
B | 0 | 3 | pre-emptive | 0 | 20
C | 0 | 2 | cooperative | 45 | 20
D | 0 | 1 (Low) | cooperative | 20 | 20
Each task consists of two processes with equal runtime (=10ms)

## Slide 78: Multicore basics - Scheduling Exercise – Single core scheduling  When will be Task A / Task C finished?
Task name | Core | Prio | Preemptive/ cooperative | Start time | Duration
A | 0 | 5 (High) | pre-emptive | 5 | 20
B | 0 | 3 | pre-emptive | 0 | 20
C | 0 | 2 | cooperative | 45 | 20
D | 0 | 1 (Low) | cooperative | 20 | 20
B
A
C
 | D |  | 
10
20
30
40
50
60
70
80
90
time
Each task consists of two processes with equal runtime (=10ms)

## Slide 79: Multicore basics - Scheduling Exercise – Multicore Scheduling  When will be Task A / Task C finished?
time
core0
core1
B
A
10
20
30 40 50
60
70
80
90
Task name | Core | Prio | Preemptive/ cooperative | Start time | Duration
A | 0 | 5 (High) | pre-emptive | 5 | 20
B | 0 | 3 | pre-emptive | 0 | 20
C | 1 | 2 | cooperative | 25 | 20
D | 1 | 1 (Low) | cooperative | 20 | 20
Each task consists of two processes with equal runtime (=10ms)
D |  | 
C

## Slide 80: Multicore basics - Scheduling Scheduling rules
 Concurrency: Tasks running in different run in parallel replicating pre-emptive behaviour
 No design decisions based on assumptions regarding task priority
 No design decisions based on assumptions regarding task distribution on different cores (Multicore scenario)
 Identification of critical issues in design phase
 Correctness by construction
 Non-Preemptive behaviour across cores cannot be ensured

## Slide 81: Backup

## Slide 82: Multicore HW: Multicore Drivers
The Limits of Singlecore Computing
Serial computing in embedded systems is hitting the technological limits
 Power wall
 Memory bandwidth wall
The Future of Information Processing
Multicore will penetrate automotive embedded systems
– as already done in PC and consumer market
The Solution
Multicore microcontrollers provide the technology to master the challenges
2006
2008
2010
2012
2014
2016
2018
2020
105
102
Computational performance,
normalized to automotive embedded performance 2005
Embedded SingleCore
MultiCore performance, embedded automotive
SingleCore performance, embedded automotive Computational performance, consumer applications
MultiCore performance, embedded automotive SingleCore performance, embedded automotive Computational performance, consumer applications
Consumer Embedded
MultiCore MultiCore
104
Free Lunch
103 is over!
heat barrier
69
Consumer
101 SingleCore
1

## Slide 83: Multicore
 In attempting a clear and crisp classification of multicore processors and MPSoCs, there are three main issues and the application itself to consider. • Thetypeofprocessingelementsuseddoingtheactualcomputation determines the choice of compilers and how specific tools need to be customized to support a specific architecture. • Thecommunicationonchipandbetweenchipsdetermineshowlong processors have to wait before data can be accessed. • Thetypesofmemoryarchitecturesusedonandoffchiphavea profound impact on latencies in the processes accessing data. • Optimizationofthehardwarearchitecturefortheapplicationrunning on them very much impacts whether the programming is straightforward, i.e. whether or not it is obvious which portions of a multicore system are running which task

## Slide 84: Multicore Key definitions used in slides
 Data coherency: All data that is communicated from one task to a different task shall be produced within one sender task execution. There shall be no mix of data from different task activations when communicating between tasks
 Time Independent:
A process/process cluster is time independent if it accepts a possible raster loss of one time period for all input values which are written from tasks outside the current task and vice versa.
The task cluster can be executed in any order to the rest of the SW
 Data Independent: There is no communication or other data dependencies between two tasks
 Re−entrancy: A function is re−entrant if it can be called on one core while it is already executing on any other core and still produce correct results for all calls
Discuss it in next session only!

## Slide 85: Multicore Key definitions used in slides
 Determinism can either refer to time (i.e. end-to-end latency) or to data values
Time determinism means, that the results, which depend on a specific set of input sequences, are made
accessible at a specific point in time or at least within a specific time interval
Value determinism means, it shall be configurable that the software system always yields the same result sequences for the same initial values and the same input sequences. This means, the calculated results (i.e. output messages or actuation values) only depend on the input values (e.g. input messages or sensor values), but not on processor load, or distribution of functions to cores
Discuss it in next session only!

## Slide 86: Multicore